## Slide 1: Automation of Programming a Galapagos Project onto FPGAs Using Docker Containers
Smile Peng

## Slide 2: Design Goals
Scalability
  Possibility of programming 100+ FPGAs at once
Simplicity
  Minimization of manual intervention
Ease of implementation
  No extra installation/set up requirements for users
    Assuming users already have Vivado, Vivado HLS, Docker installed on their host machine
Notes: The goals that were determined to be important were design for scalability, design for simplicity, and design for the ease of implementation. The design needs to be easily scalable as this automation process could possibly be used to program 100+ FPGAs at once in the future, not just 2 or 3. The design also needs to be simple/easy to use by minimizing the need of manual intervention in the form of manually entering commands etc. The design also needs to be easy to implement in such a way that it doesn’t require extra installation/set up time for the users (assuming they already have Vivado, Vivado HLS, and docker installed on their host machine). This is also a strong reason why we are using containers in the first place.

## Slide 3: Infrastructure and Container Usages
Galapagos project generating container: creates IP cores required by the Galapagos project and creates a shell file containing instructions to deploy the sender and receiver containers in parallel
Bitstream generating container: creates bitstream and sends it to the FPGA programming container (receiver)
FPGA programming container: programs received bitstream onto the FPGA
Galapagos Project Generating Container
Bitstream Generating Container (Sender Container)
FPGA Programming Container (Receiver Container)
x n FPGAs
Notes: I will quickly go over the infrastructure/how containers will be used to automate the programming of n number of bitstreams onto n FPGAs.
So 1 container will be used to generate the Galapagos project. In this container, all necessary IP cores will be generated as well as a shell file that contains instructions to deploy the n pairs of containers in parallel.
The goal of the n pairs of containers is to generate a bitstream using the output of the first container and to program that bitstream onto the mapped FPGA
These containers are the bitstream generating container (or sender container for short) and FPGA programming container (or receiver container for short). The reason the pairs are called sender and receiver is because the sender container will be sending the bitstream to the receiver container which receives the bitstream to program onto the FPGA

## Slide 4: Automation Workflow
2 main parts: 1) Galapagos project generation and 2) bitstream generation and FPGA programming
  Part 1 (Galapagos project creation): ran once on 1 container
  Part 2 (bitstream generation and FPGA programming): ran n number of times, where n represents the number of FPGA that will be programmed. This is done on n pairs of sender and receiver containers.
For multiple FPGAs, part 2 will be done in parallel
  All bitstreams will be generated and FPGAs will be programmed at the same time, hence in parallel
Notes: So the workflow of the automation has 2 main parts. The first part is the galapagos project generation and the second part is deployment of the n pairs of container to program the FPGA with its mapped bitstream.
Since the Galapagos project, the IP cores, and shell file only need to be created once, part 1 is only ran once on a single container.
However, since part 2 needs to be run for n FPGAs, it will be run n times. For multiple FPGAs, part 2 will be done in parallel meaning that bitstreams and the programming of the bitstreams will be all done all at once simultaneously instead of sequentially where this process would have one bitstream generated and programmed before another one can be generated and programmed etc

## Slide 5: Sequentially vs in Parallel FPGA Programming
Parallel: All bitstreams will be generated and programmed at the same time
    Reduces wait time drastically for many FPGAs
      Limiting factor: The time required to generate the largest bitstream
    Uses a large quantity of containers for multiple FPGAs
      1 + 2*(n number of FPGAs) containers needed
Sequentially: Each bitstream is generated and programmed onto its respective FPGA before the next FPGA can undergo the same process
    Have to wait for a bitstream to be programmed onto a FPGA before programming the next FPGA
    Unrealistically long wait time for multiple FPGA
    Uses a small number of containers (entire process can be done all on 1 container)
Notes: Here, I will compare the process of programming the FPGAs sequentially and in parallel.
Like I mentioned, all bitstreams will be generated and programmed simultaneously for in parallel. This would reduce wait time drastically for multiple FPGAs since the limiting factor is the time to generate the “largest” bitstream. However, the downfall is that it uses much more space as the process requires a large quantity of containers, it would need 1+2*n containers. So for 100 FPGAs this process would require 201 containers.
For sequentially, a bitstream is generated and programmed onto its respective FPGA before the next FPGA can undergo the same process. The major downfall of this is that the process would require an unrealistically long wait time for multiple FPGAs. IF it takes on average 2 hrs to generate 1 bitstream then for 100 FPGAs this process can take over 200 hours. The good aspect is that only 1 container would be needed.
In this situation, relating back to the design goals, in parallel was evaluated to be more appropriate. The “tradeoff” of the space is less significant than the time.

## Slide 6: Automation Steps
Galapagos project generation container is created
Needed IP cores are built with its output in a newly generated directory called hlsBuild
Shell script (createCluster.sh) that deploys n pairs of sender and receiver containers is created in Projects directory based on the mapping files (of the FPGAs) given
hlsBuild and Projects directories are retrieved onto the host machine
createCluster.sh is called on the host machine which deploys n number of pairs of containers in parallel to facilitate the generation and programming of a bitstream
  Host machine sends hlsBuild and Projects directories to the sender container
  Sender container generates the appropriate bitstream and sends it to the receiver container once the bitstream is generated
  Receiver container programs the FPGA once the bitstream is received

## Slide 7: Automation Steps
Galapagos Project Generating Container
Bitstream Generating Container (Sender Container)
FPGA Programming Container (Receiver Container)
Host machine
hlsBuild, Projects directories
Bitstream
x n FPGAs
hlsBuild, Projects directories
FPGAs
Notes: Here is the illustration of the automation steps. You can see that the first container sends the hlsBuild and Projects directory to the host machine which is then sent to the sender container when the pairs of container is deployed. Then the sender container sends the generated bitstream (which was generated using the information from the projects directory and the IP cores created and outputted in the hlsBuild directory) to the receiver which is then programmed onto the FPGA

## Slide 8: Transfer of Files
Container to container: Netcat listening port 44444
To send and receive the generated bitstream
Host to container/container to host: docker cp
To retrieve and send hlsBuild and Projects directories
Notes: I just quickly wanted to go over the transfer of file. From container to container that is done using netcat with listening port 44444. From host to container or container to host that is done with a simple docker cp command

## Slide 9: *Note: Jupyter Notebook
Before: To create a Galapagos project, code was ran on a Jupyter Notebook
Now: Converted Jupyter Notebook into python files which are ran automatically inside the container
  Reduces waiting time
Jupyter Notebook files are still available for users
  Tutorial like, contains thorough information about what Galapagos is and what each section of code accomplishes in the project creation/bitstream generating process
Notes: I just wanted to go over a quick note of Jupiter notebook. Originally, to create the Galapagos project, the code was run on a Jupyter Notebook (which if you are not doing it for the first time is quite a tedious process since you have to wait for the code to run before moving on to the next set of code). Now, I converted the notebooks into python files which are automatically ran inside the container which can reduce the wait and supervision time. But I have kept the Jupiter notebook files in the Galapagos directory anyways since it is very informative and tutorial like. It goes through a lot of information about Galapagos and what each section of code accomplishes which I think would be very useful for users when they run this process for the first few rimes.